## Slide 1: Lan Mode Principle / Implementation
31 July 2017
Benson Chuang

## Slide 2: Agenda
What’s Lan mode
Lan mode operation
Implementation
  API
  Key Exchange
  Encryption, Decryption, Encapsulation
Lan Mode Simulation

## Slide 3: What’s Lan Mode

## Slide 4: Lan Mode Goals
Reduce latency of event generation and consumption, without compromising security or power management.
Enable Module to Mobile Application communication when the Device Service is not reachable.
Module supports up to two simultaneous LAN mode mobile applications.

## Slide 5: Lan Session Topology
Ayla Module
Lan Parameters
(Uploaded by command queue)
LAN Status : enable
Auto Sync : 1
LAN IPKEY : qT+auR+3FclF4gW48kjGRItQU3XdNg==
LAN KEY ID : 813
Keep alive : 30
Lan session
Device session
Cloud session
http server
http server
http client
http client
MCU

## Slide 6: Lan Mode Operation

## Slide 7: Start LAN Mode Session
http server
http client
Establish LAN Mode Session
202
http client
1
2
Key Exchange
http server
random_1
time_1
random_2
time_2
200
3
LAN Mode Enabled
Ayla Module
MCU

## Slide 8: Ask Datapoint from Device
http server
http client
Notify Device
200
http client
1
2
Get command
http server
200
Property Name
http server
http client
3
Post Datapoint
200
Property Name
Value
MCU
Ayla Module
2.1
req
res

## Slide 9: Post Datapoint to Device
http server
http client
Notify Device
200
http client
1
2
Get command
http server
200
Property Name
Type
Value
MCU
Update
Ayla Module
2.1
ADS
2.2
Update

## Slide 10: Keep Lan Mode Session
http server
http client
Keep Alive
200
Ayla Module

## Slide 11: Implementation

## Slide 12: Device/Cloud LAN Mode Function
LAN session:
Retrieve lankey
Establish LAN Mode
Notify device
Keep Alive
Key Exchange
Get command
Post datapoint
Implement following URI at both Device and Clouds’ HTTP server

## Slide 13: Retrieve lankey
URI=/apiv1/devices/<$ID>/lan.json
METHOD=GET
200=Success
ADS – Get Lan configuration
Req: Lan configuration
LAN Status : enable
Auto Sync : 1
LAN IPKEY : qT+auR+3FclF4gW48kjGRItQU3XdNg==
LAN KEY ID : 813
Keep alive : 30
Res: Lan configuration

## Slide 14: Establish Lan Mode Session
LAN API– APP establish Lan configuration
14
Copyright © 2015 Ayla Networks
Establish Lan session
URI=/local_reg.json
METHOD=POST
202=Accepted
http server
http client

## Slide 15: Notify Device
LAN API– Ask device get command from APP
15
Copyright © 2015 Ayla Networks
Notify Device
URI=/local_reg.json
METHOD=PUT
202=Accepted
http server
http client

## Slide 16: Keep Alive
LAN API– Keep Alive
16
Copyright © 2015 Ayla Networks
Keep Alive
URI=/local_reg.json
METHOD=PUT
202=Accepted
http server
http client

## Slide 17: Key Exchange
LAN API– Calculate a cipher suite
17
Copyright © 2015 Ayla Networks
Key Exchange
URI=/local_lan/key_exchange.json
METHOD=POST
200=Accepted
http client
http server

## Slide 18: Get command
LAN API– Retrieve the command from APP
18
Copyright © 2015 Ayla Networks
Get command
URI= /local_lan/commands.json
METHOD=GET
200=Accepted
http client
http server
1.1
1.2
Have command
No command
Encapsulation
2

## Slide 19: Post datapoint
LAN API– Send datapoint to APP
19
Copyright © 2015 Ayla Networks
Post datapoint
URI /local_lan/property/datapoint.json
METHOD=POST
200=Accepted
http client
http server
Decryption

## Slide 20: Key Exchange Detail

## Slide 21: Key Exchange – 1. Exchange Key Pairs
21
Copyright © 2015 Ayla Networks
http server
http client
Establish LAN Mode Session
202
http client
1
2
Key Exchange
http server
random_1
time_1
random_2
time_2
200
Ayla Module
Device sends 16 bytes random string along with current time to APP
APP generate 16 bytes random string along with current APP time to Device
Calculate IV seed and sign at both sides(APP and Device)

## Slide 22: Key Exchange – 2. Algorithm
22
Copyright © 2015 Ayla Networks

## Slide 23: Key Exchange – 3. Calculation – APP Key
23
Copyright © 2015 Ayla Networks
1
2
3
0

## Slide 24: Key Exchange – 4. Calculation – Device Key
24
Copyright © 2015 Ayla Networks
1
2
3
0

## Slide 25: Encryption, Decryption, Encapsulation

## Slide 26: Encryptor
Only initial encryptor once when doing Key Exchange
Encryptor is encrypted string by using CBC with AES 256
Encryptor is stateful
encryptor = AES.new(str(self.appCryptoKey), AES.MODE_CBC, str(self.appIvSeed))

## Slide 27: Encryption and Encapsulation - 1
The response format of GET command sent by device
27
Copyright © 2015 Ayla Networks
newcommand
1
2
1
2
3
3
Padding, 16-byte alignment

## Slide 28: Encryption and Encapsulation - 2
The response format of GET command sent by device
28
Copyright © 2015 Ayla Networks
4
4
encrypted_data = encryptor.encrypt(padding_data)
5
5
encryptedb64 = base64.b64encode(encrypted_data)
6
newcommand
7
6
sign = HMAC.new(str(appSignKey), enclist_str, SHA256)
signb64 = base64.b64encode(sign.digest())
7

## Slide 29: Encryption and Encapsulation - 3
The response format of GET command sent by device

## Slide 30: Decryptor
Only initial decryptor once when doing Key Exchange
Decryptor is stateful
decryptor = AES.new(str(self.devCryptoKey), AES.MODE_CBC, str(self.devIvSeed))

## Slide 31: Decryption
When APP receives datapoint update from device
1
2
3
1
3
2

## Slide 32: Lan Mode Simulator

## Slide 33: Architecture
CLI
Config
lansession
lanbridge
HTTP
Server
lansession
lansession
lansession
Set prop
Get prop
Callback
Commands
Datapoints
Ayla Module
Display
module
POST/PUT local_reg
IP
demux

## Slide 34: Appendix

## Slide 35: Reference
Wi-Fi Module REST API Specification
AMAP Source Code
DeviceParadise : Module log interpreter
GetAllProperty is not supported by Ayla Production Agent(BlackBox)

## Slide 36: Thank you
WWW.AYLANETWORKS.COM